## Slide 1: Realtime debugging of a softcore OpenRISC CPU
Jules Peyrat
14 november 2025

## Slide 2: Context
CS473 Course Material
  Lattice ECP5 FPGA (« Gecko5Education »)
  Running a softcore OpenRISC CPU (OR1300)
  Toolchain to compile C programs for the or1k (OpenRISC 1k) CPU
At the moment, GDB is not compatible with the softcore CPU
We would like students to be able to debug their programs using GDB
Step-by-step execution, check register and memory content

## Slide 3: Objective
GDB & User
Front End
SW/HW Bridge
Lattice ECP5 FPGA
« Gecko5Education »
Target CPU
Debug
Controller
TAP Controller
System Bus
OR1300

## Slide 4: Overview
The JTAG Standard & Interfacing JTAG
Using OpenOCD (Open On-Chip Debugger)
Debug Controller
Interfacing the System Bus

## Slide 5: 1/ The JTAG Standard
OR1300

## Slide 6: 1/ The JTAG Standard
Join Action Test Group
HW communication protocol for debugging SoC’s
Five signals
  TCK (JTAG clock)
  TDI, TDO (input and output bit lines)
  TMS (next slide)
  Async reset
Instructions
  BYPASS (TDI = TDO)
  IDCODE (32bit SoC info: manufacturer, revision….)
  DEBUG

## Slide 7: 1/ The JTAG TAP Controller
TAP (Test Access Port) Controller = implements a FSM
Example: 32-bit stall command
  Select DEBUG instruction (IR)
    TMS = 1  Select-DR-Scan
    TMS = 1  Select-IR-Scan
    TMS = 0  Capture-IR
    TMS =  Shift-IR
    Send data through TDI…. (TMS=0)
    TMS = 1  Exit-IR
    TMS = 1  Update-IR
    TMS = 0  Run-Test/Idle
  Send data through DR
    Same but skip cycle 2
Use of shift registers
Instruction/Data Register
TDO
TDI

## Slide 8: 1/ The JTAGG Primitive
What or1k wants us to do
  Use a provided softcore TAP controller
  Artificially create a JTAG interface
What we want to do
  Use the hardware JTAGG primitive of our FPGA
  Same component used for reconfigurating the FPGA
Problem
  No direct access to the TDI signal
  TDI is 1-cycle late
  Solution = delay by 1 the Shift-DR state signal

## Slide 9: 2/ OpenOCD
SW/HW Bridge
OR1300

## Slide 10: 2/ OpenOCD
HW/SW bridge through JTAG
To work, OpenOCD needs
  IR and DR shift register lengths…
  IR instruction code…
  Debug controller command formats…
Problem
Using an « unsupported » TAP controller (the one from the FPGA)
Need for an adapted OpenOCD driver
Very close to an existing driver! (mohor)
BSD file of the OpenOCD-supported TAP controller

## Slide 11: 3/ Debug Controller
OR1300
Debug
Controller

## Slide 12: 3/ Debug Controller
OR1200-supported version provided by or1k project
Composed of 4 submodules
Needs refactoring:
  Using JTAGG requires to adapt the input shift register logic (1 cycle delay problem)
  Not the same bus architecture (next slide)
At the moment, the input shift register logic somewhat works (under a certain input shift register size threshold. Above => bit flips)
CPU0 Submodule
CPU1 Submodule
Wishbone Submodule
JSP Submodule
reg_module_id
CPU0
CPU1
Debug Controller
SoC
Wishbone Bus
JTAG

## Slide 13: 4/ System Bus
The OR1200 CPU uses a Wishbone bus architecture
Our OR1300 CPU uses a different bus architecture
Example of difference:
  OR1300 has one 32-bit for both address and data. Address is provided at the beginning of a transaction.
  OR1200 has two 32-bit buses for both address and data.
Wishbone Submodule
Bus Interface Unit
JTAG Command Logic

## Slide 14: Future work
Implement the OpenOCD driver
Fix the JTAGG interfacing problem
Write a dummy debug controller for dummy memory reads and CPU states
Test the whole setup with GDB
Re-implement the BIU to support the OR1300 bus
  Perform memory reads from GDB
  Upload programs using GDB
Link the CPU debug submodule to the OR1300 CPU
  Stall the CPU
  Step-by-step execution

## Slide 15: Thank you